## Slide 1: 4. Construction Systems of Hall Buildings

## Slide 2: Construction Systems of Hall Buildings
Hall buildings allow the creation of free spaces with little or no internal support. The characteristic feature of hall buildings is a large ground plan and a relatively small height.
The hall object can also include internal built-in floors with different height requirements: Two-storey x Large-scale halls x Combined monoblocks.
Hall objects are used especially for: cultural x sports x manufacturing and storage x traffic purposes.
In most cases, hall objects have a split supporting function and cladding.

## Slide 3: Bending Construction Systems
The basic element is a bend-loaded, simply inserted or interlocking element that transmits primarily vertical loads.
Plate system - are made up of different types of boards (with reinforced ribs, cellars…
Trusses system - consists mainly of the roof trusses (beam elements) deposited on the columns, beams or walls.
Frame systém - transfers the frame bending moment to the frame stand as a result of the rigid connection.

## Slide 4: Compressive Construction Systems
If the arc shape or flat structure designed in the shape of the load pressure line, the structure transmits pressure loads.
Arc structural systems - designed for buckling pressure in combination with a bend.
Flat compressive construction systems – vaults - are loaded with buckling pressure and bending
Flat compressive construction systems – shell - have a small structural thickness and the bending loads are transmitted only to a limited extent.
Rod structural system - have to a certain extent similar effects as a flat construction of the same shape.
Folded slab structure system - is formed from flat triangular elements creating a rigid spatial system

## Slide 5: Tensile Construction System
The tensile construction system includes suspension systems, pneumatic systems and suspended systems.
The suspension systems - may be truss, panel, cable and membrane structures.
Pneumatic systems - are carried by overpressure of the internal air.
Suspended systems - the principle of the suspended system is the suspension of the roof beam by means of bars anchored to pressed pilots, arcs or frames, etc.