## Slide 1: 5. Dilatation of Buildings

## Slide 2: Dilatation of Buildings
The construction joint - distance between the two building blocks.
The expansion joint - divides buildings (parts) into smaller rigid units.
Unforced effects include:
  Volume changes due to temperature
  Volume changes due to moisture
  Rheological effects (creep and shrinkage)
  Changing the shape of the foundation joint (bottom surface)
Expansion joints eliminate: Static effects x Dynamic effects x Acoustic effects x Heat-technical effects.

## Slide 3: Volume Changes
Volume changes can be caused by:
  Changing the temperature of the external and internal environment (thermal expansion of materials).
  Changing the moisture of the materials (drying and swelling)
  Rheological changes of the materials (Shrinkage x Creep)
Stress elements due to volume changes can lead to:
  Element breakage by tensile cracks
  Compression element failure
  Expanding effect on surrounding structures
  Creation and expansion of joints between element and surrounding structures
  Rheological changes of materials

## Slide 4: Structural principles and structural solutions
Maximum distance of expansion joints in masonry with lime mortar:
  burnt bricks 100 m
  sand-lime bricks 50 m
  concrete blocks 50 m
  natural stone 60 m
  reinforced concrete 40 m
Construction design of the expansion joints:
  Duplication of supporting structures
  Unilateral sliding fit
  Cantilevered ceiling structure
  Inserted field with slide bearing

## Slide 5: Uneven Settling
Irregularities in the substructure of the object - irregular and oblique loading of soil layers with different compressibility, different levels of groundwater level, undermined area, additional changes in the subsoil or level of ground water level.
Different loads in the footing bottom - different height of the part of the building, different utility loads in different parts of the building, inappropriate design of the area of individual flat foundations
Different foundation structures of parts of the building - the combination of shallow and deep foundations
The time interval between the realizations of the different units of the building - the new part follows the older one, where the settlement has already taken place.

## Slide 6: Structural principles and structural solutions
Design principles for expansion joints:
  Expansion joints must allow vertical displacements
  Expansion joints pass through the whole object, including the foundations
  Foundations must not interfere with one another
  Must comply with the required thickness joints
Design solutions for the implementation of expansion joints:
  Sided cantilevered horizontal structures
  Reversible cantilevered horizontal structures
  Fields inserted
  Modulation adjustment